# Porting Contiki-NG to EFR32ZG28 (ARM Cortex-M0+):
## Project Title:
Porting Contiki-NG to EFR32ZG28 Platform
## Objective
To enable Contiki-NG RTOS on the EFR32ZG28 SoC (Cortex-M0+) by:
- Creating a new platform definition under arch/platform/efr32zg28/
- Building and running a sample application (LED blink)
## Target Platform Details
Component	Description
CPU Core	ARM Cortex-M0+
RTOS	Contiki-NG
Toolchain	arm-none-eabi-gcc

## Structure Setup
contiki-ng/
├── arch/
│ ├── cpu/
│ │ └── efr32/
│ │ ├── efr32.c
│ │ ├── efr32-clocks.c
│ │ └── efr32-startup.c
│ └── platform/
│ └── efr32zg28/
│ ├── platform-conf.h
│ ├── contiki-conf.h
│ ├── efr32zg28.c
│ ├── leds-arch.c
│ ├── syscalls.c
│ ├── gpio-hal-arch.c
│ ├── startup_efr32zg28.S
│ ├── efr32zg28.ld
│ └── Makefile.platform
├── examples/
│ └── efr32zg28/
│ └── led_blink.c

## File Descriptions and Roles
### Platform Folder (arch/platform/efr32zg28/)
File Name	Purpose
platform-conf.h	Hardware-specific configuration
contiki-conf.h	Contiki config (defines, macros)
efr32zg28.c	Platform initialization
leds-arch.c	GPIO control for onboard LEDs
gpio-hal-arch.c	GPIO HAL interface
syscalls.c	Minimal newlib syscall stubs
startup_efr32zg28.S	Startup assembly file
efr32zg28.ld	Linker script for memory layout
Makefile.platform	Lists source files for platform

### CPU Folder (arch/cpu/efr32/)
File Name	Purpose
efr32.c	Generic CPU initialization
efr32-clocks.c	Clock configuration
efr32-startup.c	Reset vector handler

### Example Folder (examples/efr32zg28/)
File Name	Purpose
led_blink.c	Example app for testing LEDs

## Build Process
>>cd contiki-ng/examples/efr32zg28/
>>make clean
>>make TARGET=efr32zg28 led_blink V=1
Issue: TARGET not defined / Platform does not exist